## Slide 1
ECE 471
Communication Theory
Presentation by:
Jenny Doan
Daniel Noyes
802.11
Standards

## Slide 2: What is the 802.11 Standard?
IEEE standard for wireless communication.
Allows roaming computers to talk to other devices through a peer to peer network.
Also allows devices to connect to each other via an access point or extension point which is the transmitter or receiver.
This allows users to share and exchange data with one another.

## Slide 3: Spread Spectrum
The carrier signals occur over the full bandwidth or spectrum of a device's transmitting frequency.
Transmit with a unique spreading code.

## Slide 4: Frequency Hopping Spread Spectrum (FHSS) Block Diagram 802.11

## Slide 5: Frequency Hopping Spread Spectrum (FHSS) 802.11
Uses 79 separate 1 MHz channels
Hops about every 0.1 sec (2.5 hop/sec)
Pseudo random hopping pattern
Gaussian Frequency Shift Keying
Immune to single frequency noise, has trouble with wideband noise

## Slide 6: Direct Sequence Spread Spectrum (DSSS) Block Diagram 802.11, 802.11b

## Slide 7: Direct Sequence Spread Spectrum (DSSS) 802.11 and 802.11b
Phase-Shifts a sine wave pseudorandomly with a continuous string of pseudonoise (PN) code symbols called "chips".
Transmission Method: Multiply the data being transmitted by the PN.
  The PN is a sequence of 1 and -1 values at the chip rate. This rate is much higher than the original signal rate.
Modulation
  Differential Binary Phase Shift Keying
  Differential Quadrature Phase Shift Keying

## Slide 8: Encoding with 11-chip Barker sequence 802.11b
Used only at 1 and 2 Mbits/sec, CCK is used at higher bit rates 5.5 and 11 Mbits/sec

## Slide 9: DSSS Benefits 802.11 and 802.11b
Benefits:
  Resistance to intended or unintended jamming
  Sharing of a single channel among multiple users
  Reduced signal/background-noise level hampers interception
  Determination of relative timing between transmitter and receiver

## Slide 10: Complementary Code Keying (CCK) 802.11b
Supplement the Barker Sequence to achieve higher data rates than 2Mbps at the expense of a shorter distance.
  Because of shorter chipping sequence (8 vs. 11)
Encode more bits
  4 chipping sequences at 5.5 Mbps and 64 chipping sequences at 11 Mbps

## Slide 11: Signal being modulated with FHSS vs. DHSS 802.11

## Slide 12: Orthogonal Frequency Division Multiplexing 802.11A, 802.11G, 802.11N, 802.11AC Block Diagram

## Slide 13: Orthogonal Frequency Division Multiplexing (OFDM) 802.11A, 802.11G, 802.11N, 802.11AC
Multi-Carrier Modulation
Immunity to selective fading
  Divide overall channel into multiple narrowband signals
Resilience to interference

## Slide 14: QAM: Quadrature Amplitude Modulation 802.11A/B/G/N - 64 QAM 802.11AC - 256 QAM
Communication Method to transfer higher data rate in one signal.
Encode bits based on a Amplitude and Phase.
Higher QAM will lead to transmitting of more bits per symbol. This can also lead to noise error due to the points being closer together.
Higher bit encoding means higher error rate.
Lower QAM is more reliable than higher QAM

## Slide 15: QAM Simulation 802.11 G & 802.11AC
Encoding a 16-QAM Signal
QAM Constellation was set up with a gray code approach to minimize error bits.
Created through MATLAB Simulink Rectangular QAM routine.

## Slide 16: Reason For Grey Code
Minimize bit error to one bit change
Example shows various points affected by noise. These changed to another Symbol encoding.

## Slide 17: MIMO
Allows multiple inputs and outputs.
Able to communicate simultaneously to more devices.
Increase data transmission

## Slide 18: Common Standards Used Today
802.11G
Date of Approval: June 2003
Maximum Data Rate: 54Mbps
Modulation
  CCK
  DSSS
  OFDM
RF Band: 2.4GHz
Channel Width: 20MHz
802.11N
Date: Oct 29, 2009
Maximum Data Rate: 600Mbps
RF Band: 2.4 or 5GHz
Modulation
  CCK
  DSSS
  OFDM
4 spatial streams
Channel Width: 20 or 40 MHz
Introduction to MIMO
Antenna Technology
Backwards compatible

## Slide 19: Future 802.11 Standards
802.11AC
  Date of Approval: January 2014
  Builds upon the 802.11n
  Wider Channels (80 or 160 MHz)
  5GHz Frequency Band
  More spatial streams (8 vs. 4)
    433.3Mbps per stream (80 MHz channel)
  Higher order modulation (256-QAM vs. 64-QAM)
  Addition of a MU-MIMO
Other standards will be built upon the 802.11AC

## Slide 20: Current 802.11 Specifications
Standard: | Max Data Rate: | Modulation: | Freq Band: | Bandwidth:
802.11 | 2 Mbit/s | DSSS,FHSS | 2.4 GHz | 22 MHz
802.11A | 54 Mbit/s | OFDM | 5 GHz | 20 MHz
802.11B | 11 Mbit/s | DSSS | 2.4 GHz | 22 MHz
802.11G | 54 Mbit/s | OFDM,DSSS | 2.4 GHz | 20 MHz
802.11N | 600 Mbit/s | OFDM | 2.4/5 GHz | 20/40 MHz
802.11AC | ~1 Gbit/s | OFDM | 5 GHz | 20/40/80/160 MHz

## Slide 21: Learn From class correlations to the standard
With all of this, now you can see why Communication Theory is important in our daily lives.

## Slide 22
Questions?

## Slide 23: References
ieee1451.nist.gov/Workshop_04June01/Gilsinn.pdf
http://www.slideshare.net/AbhishekPachisia/ieee-80211-15604512
http://www.radio-electronics.com/info/wireless/wi-fi/ieee-802-11g.php
http://www.radio-electronics.com/info/rf-technology-design/ofdm/ofdm-basics-tutorial.php
http://eeemea.in/wp-content/uploads/2014/02/mimo-general-outline.gif
https://upload.wikimedia.org/wikipedia/commons/thumb/4/4e/OFDM_transmitter_ideal.png/754px-OFDM_transmitter_ideal.png
https://upload.wikimedia.org/wikipedia/commons/thumb/9/90/OFDM_receiver_ideal.png/800px-OFDM_receiver_ideal.png
people.cs.clemson.edu/~westall/851/fhss_dsss.pdf
http://sharmamonika95.blog.com/files/2012/10/dsss1.gif
http://grouper.ieee.org/groups/802/11/ieee802-11-logo.jpg
http://rfmw.em.keysight.com/wireless/helpfiles/89600B/WebHelp/subsystems/wlan-ofdm/Content/resources/image/ofdm%20orthogonalspacedsubcarriers.png