# Problem 2.7a:
Sample length:
>>n = -10:10;
h[n] = 2δ[n+1] – 2δ[n-1]
>> h = 2*(n == -1) - 2*(n == 1);
x[n] = δ[n] + δ[n-2]
>> x = (n == 0) + (n == 2);
y[n] = x[n] * h[n]
>> y = conv(h,x);
Set up the new length for the convolved function
>> ny = 2*n(1):2*n(end);
Plot the new vector y
>> stem(ny,y)
Insert graph info
>> title('title');
>> xlabel('x');
>> ylabel('y');

# Problem 2.7b:
In this Problem you consider two finite length sequences and check with the length of y[n] =(M + N -1)
In this section you have to prove that both sequences h[n] and x[n] with h length be a to b and x from c to d.

When you analyse the conv function you notice that the only compute up to Nx + Nh -1 samples so the output of the new converged function y[n] will have a length of number of h and x together minus 1. since both have a variable length of h:a-b and x:c-d we can see that the new n length is from (a+c) to (b+d) which turns out to be both length added together minus 1.

# Problem 2.7c:
Book given values
>> a = 0;
>> b = 24;
>> c = -2;
>> d = 14;;
>> nx = [a:b];
>> nh = [c:d];
Calculate: x[n] = (1/2)^(n-2) u [n-2]
>> x = (1/2).^(nx - 2) .* ((nx-2) >= 0);
Calculate h[n] = u[n+2]
>> h = ((nx+2) >=0);
Find the convolution:
>> y = conv(h,x);
>> ny = (a+c):(b+d);
Plot the values of y[n]
# Problem 2.7d:
Book given values
>> n = [0:99]; %100 values
Calculate: x[n] = cos(n^2)*sin(2*pi*n/5)*u[n]
>> x = cos(n.^2).*sin(2*pi.*n/5).*(n >=0)
Calculate h[n] = (0.9)^n * (u[n] - u[n-10])
>> h = (0.9).^(n) .*((n>=0) - ((n-10)>=0));
Find the convolution:
>> y = conv(h,x);
>> ny = n(1)*2:n(end)*2;
Plot the values of y[n]
>> stem(ny,y)

# Problem 2.7e:
Book given values
>> Length = 50;
>> n = [0:99]; %100 values
Calculate: x[n] = cos(n^2)*sin(2*pi*n/5)*u[n]
>> x = cos(n.^2).*sin(2*pi.*n/5).*(n >=0)
Calculate h[n] = (0.9)^n * (u[n] - u[n-10])
>> h = (0.9).^(n) .*((n>=0) - ((n-10)>=0));
Separate the Values of x and n to two different segmetns:
>> x0 = x(1:L);
>> x1 = x(L+1:2*L);
>> n0 = n(1:L);
>> n1 = n(L+1:2*L);
find the convolution of each seperate part and add them together
>> y0 = conv(h,x0);
>> ny0 = n0(1): (n0(end)*2+L);
>> y1 = conv(h,x1);
>> ny1 = n1(1): (n1(end)*2);
>> nyy = ny0(1)*2: ny1(end);
>> yy = zeros(1, length(nyy));
Now you go through and add all the data together
For look for the code to add after each other
for i = 1: length(yy)
if(i <= L)
yy(i) = y0(i);
else
if(i < length(y0))
yy(i) = y0(i) + y1(i-L);
else
yy(i) = y1(i-L);
end
end
end
Plot with the trimmed graph same as d